May 2020

Inspection Form and Instructions for

Best Management Practice (BMP) Compliance

BMP inspections are conducted at facilities using more than household quantities of regulated substances in conjunction with local efforts to protect sources of drinking water. The inspections are conducted to ensure that each potential contamination source (PCS) is complying with New Hampshire’s BMPs for Preventing Groundwater Contamination Rule, Env-Wq 401, so that the risk of groundwater and/or surface water contamination in the source protection area is minimized

| Section 1. Inspection Preparation | Follow the steps in this section to ensure that your inspections are conducted in a thorough and professional manner and to minimize the inconvenience to the PCS. |
| --- | --- |

1. Know the BMP Rules.  Knowledge of the Env-Wq 401 BMP rules will enable you to know what to look for during a inspection. It is important to conduct your inspections as efficiently as possible so that you don’t waste your time or that of the PCS. Knowing the BMP rules will speed up an inspection, prevent oversights, and is essential to discuss compliance issues.

2. Be sure each PCS has received a copy of the Env-Wq 401 BMP rules and NHDES fact sheet summarizing the BMP Rules in advance of your appointment to do the inspection. Ask them to read the rules and offer to answer any questions before the inspection. Many PCSs become more comfortable about an inspection after realizing the “common sense” approach of the BMP rules. Bring several BMP fact sheets to each inspection to distribute to the PCS representative(s).

3. Know your Source Water Protection Area. During an inspection keep in mind where the PCS is situated relative to your source(s).  This may help you make site-specific decisions about compliance issues. Bring a map showing your protection area(s) to the inspection so the PCS can see that they are located inside the protection area.

4. Know your Source Water Protection Area Management Plan. Keep in mind the compliance mechanism of your management plan. One of the most commonly asked questions by PCSs is “How are the BMP rules enforced?” so you should be able to explain how you will achieve compliance with BMP violations. Emphasize that you will seek the least costly and most practical way to achieve compliance. Voluntary compliance is always the goal.

5. Find out as much as you can about a PCS before you go to the inspection. It saves time to know site -specific background information, such as: what type of sewage disposal system does the PCS have; how long has the PCS been in business; and what was the historic usage of the PCS’ property. Also, before the inspection, think about site-specific concerns pertaining to the storage, handling and disposal of regulated materials. For example, before conducting an inspection at a printing company, anticipate that you will need to know how they store, handle and dispose of ink products. Knowing key background data and anticipating site-specific compliance concerns will help prevent oversights and will make the inspection more efficient.

6. Be sure that the PCS understands that a BMP inspection is mutually beneficial. Explain that the Env-Wq 401 rules apply to all PCSs in New Hampshire, not just the ones within a source protection area. Also, explain that compliance with BMP rules may benefit them by improving their environmental practices; reducing their overall environmental liability; and perhaps minimizing potential cleanup costs by preventing a release of hazardous substances. Your water system benefits from improved protection of your drinking water sources and reduced sampling costs.

7. If at all possible, fill out Sections 2, 3, and 4 of this form before you go to the PCS. Most PCS representatives are busy and will appreciate whatever you can do to minimize your time there. This is a good time to think about the site-specific concerns mentioned in (5) above.

8. Know the BMP inspection form. During an inspection, it is not always possible to fill out the form in the same order as the questions are written. Knowing the form makes it much easier to “skip around” while you are touring a facility.

Section 2.

Record of Inspection						Fill out Sections 2 and 3 prior to each inspection.

| Inspection Date |  |
| --- | --- |
| Potential Contamination Source (PCS) |  |
| Town Where PCS Is Located |  |
| Agency Conducting Inspection |  |
| Name and Title of Person(s) Performing Inspection | 1. |
|  | 2. |
|  | 3. |
| Name and Title of Person(s) Giving Information about the PCS | 1. |
|  | 2. |
|  | 3. |

Section 3.

Potential Contamination Source (PCS) Information      Update this section for each 3-year inspection.

| PCS Name |  |
| --- | --- |
| PCS Address |  |
| PCS Phone Number |  |
| PCS Tax Map and Lot Number | Tax Map | Lot no. |
| PCS Owner |  |
| PCS Owner Address (If different from above) |  |
| General Description of Business |  |

Section 4.

Inventory Verification

Complete Steps A., B. and C. below.

An “inventory verification” is conducted before the actual inspection to find out if the PCS uses greater than household quantities of regulated substances, thereby making it subject to the Env-Wq 401 BMP rules. If the PCS does not use greater than household quantities of regulated substances, answer “no” in Step C. and do not complete the rest of this form. This verification may be performed by phone.

Step A. What regulated substances does the PCS use, handle, or store?

The best way to complete this section is to ask the PCS contact to fill out the chart below. If possible, arrange to have the PCS fill out this chart before you arrive to do the inspection. If not done earlier, this section is filled out as the first task of your inspection. Quantities listed below only need to be estimates of maximum quantities on hand at any one time. Any chemicals stored in regulated tanks should be included on this chart.

| Regulated Substance | Quantity (gallons) | Regulated Substance | Quantity (gallons) |
| --- | --- | --- | --- |
| Transmission and brake fluid |  | Cleaners and Disinfectants |  |
| Radiator coolants |  | De-icing salt |  |
| Hydraulic fluid |  | Refrigerants |  |
| Motor oil |  | Fertilizer |  |
| Waste oil |  | Pesticides and herbicides |  |
| Gasoline or jet fuel |  | Photo processing chemicals |  |
| Diesel Fuel and kerosene |  | Printing ink |  |
| #2 Heating oil |  | Lye or caustic soda |  |
| Grease and lubricants |  | Metal buffing compounds |  |
| Degreasers |  | PCBs (bulk) |  |
| Battery acid (bulk) |  | Products labeled “poison” |  |
| Rustproofers |  | List other products you think are hazardous, below: |
| Car wash products |  | 1. |  |
| Asphalt and roofing tar |  | 2. |  |
| Paint, stain, urethane |  | 3. |  |
| Thinner, wood stripper |  | 4. |  |
| Waterproofing chemicals |  | 5. |  |
| Dry-Cleaning Fluids |  | 6. |  |

Section 4.

Inventory Verification (continued)

Step B. What regulated substance wastes does the PCS produce?

The second part of the inventory verification is to find out if the PCS produces any regulated substance wastes and, if so, how they are disposed. As done for Section A, if possible arrange to have the chart below filled out by the PCS contact prior to your inspection. If not done ahead of time, fill out the chart after you look over the results of Section A. For example, if the PCS is a machine shop that uses cutting oils and degreasing solvents, then the chart below must indicate how they dispose of their waste oils and used solvents. Do not list non-hazardous wastes, such as refuse and paper on this chart. Estimates of quantities generated per year are adequate.

| Type of Waste | Quantity Generated per Year | Disposal Method |
| --- | --- | --- |
| 1. |  |  |
| 2. |  |  |
| 3. |  |  |
| 4. |  |  |
| 5. |  |  |

Step C. - Are greater than household quantities of regulated substances or wastes used, handled, or stored?

If all containers at the PCS are less than 5 gallons, check “NO” below.

(Check the appropriate box below.)

√ Check Below

|  | YES | Greater than household quantities of regulated substances or wastes are used, handled, or stored so conduct an inspection to determine compliance with BMP rules. |
| --- | --- | --- |
|  | NO | Greater than household quantities of regulated substances or wastes are not used, handled, or stored so do not conduct an inspection to determine compliance with BMP rules. |

If you checked “NO” above, do not continue with the inspection because the inventory verification indicated that regulated substances are not used by the PCS.

If you checked “YES” above, complete the rest of this form, which contains a series of questions that need to be answered to assess if the PCS is in compliance with the BMP rules. Be sure that you answer all of the questions – indicate ”n/a” if that is the correct answer.

PCSs that have underground tanks, but no other containers larger than 5 gallons are special cases. If a PCS fits that description, you should not conduct a full inspection. List the USTs in Section 7, verify that the USTs are registered with NHDES, and then stop the inspection. Convenience stores and self-service gas stations are common examples.

| Section 5. Regulated Substance Storage Areas | If you observe a BMP violation during an inspection, point it out to the PCS contact and discuss it right away - inspections are meant to benefit both parties. |
| --- | --- |

Storage practices of regulated substances, whether raw materials or wastes, are a major focus of the BMP rules. Therefore, one of the most important tasks of an inspection is to observe all areas where the regulated substances listed in Section 4 - Steps A and B are stored.  Ask the PCS contact where they store their regulated substances and list them below. Then be sure to carefully observe each interior and exterior storage area to see if their storage practices comply with the BMP rules. Consider at all times during your observations that you are looking for practices that could lead to a potential release of hazardous substances to the environment.  Use common sense.

Step A. - List and briefly describe all on-site storage areas below.

Exterior Storage Areas

1.

2.

3.

4.

Interior Storage Areas

1.

2.

3.

4.

Summary of Env-Wq 401 BMP rules pertaining to storage of regulated substances

- Secure storage areas against unauthorized entry.

- Store regulated substances on an impervious surface.

- Inspect storage areas weekly.

- Cover regulated containers in outdoor storage areas.

- Regulated containers in outdoor storage areas must be more than 50 feet from surface water, 50 feet from storm drains, 75 feet from private wells, and more than 400 feet from public wells.

- Secondary containment is required for outdoor storage of regulated containers.  On-premise use heating oil tanks are exempted, however, containment is still recommended.

- Regulated containers should be clearly and visibly labeled.

| A regulated container is a container with a capacity of 5 gallons or more that contains hazardous substances. Multiple 5-gallon containers of a regulated substance may qualify the facility as a PCS. | Secondary containment means an impervious structure adequate to hold 110% of the volume of a regulated container. |
| --- | --- |

| Section 5. Regulated Substance Storage Areas (continued) | Proceed at a comfortable pace as you tour a facility. You may miss key observations if you go too fast. Step B. Questions to ask when observing outdoor storage areas. |
| --- | --- |

Storage of Regulated Substances in outdoor storage areas

(refer to Env-Wq 401.04)

*	Yes	No	N/A	1.  Do the outdoor storage area(s) have an impervious surface under the regulated substances? (Wooden

floors with earth beneath are not impervious surfaces.)		Env-Wq 401.04(b)

Describe: __________________________________________________________________

__________________________________________________________________________

*	Yes	No 	N/A	2.  Is the outdoor storage area(s) secured against unauthorized entry (fence, surveillance, etc.)?

Env-Wq 401.04(c)	     	     Describe: __________________________________________________________________

*	Yes	No 	N/A	3.  Is the outdoor storage area(s) inspected at least weekly for signs of spills?

Env-Wq 401.04(d)

*	Yes	No 	N/A	4.  Is there sufficient space between large containers to allow for inspections?

Env-Wq 401.04(d)

*	Yes	No	N/A	5.  Is each regulated container clearly and visibly labeled with the name of material?

Env-Wq 401.04(e)

*	Yes	No	N/A	6.  Is each container closed and sealed or equipped with a drip pan beneath a spigot, valve or

Env-Wq 401.04(f)		pump?

*	Yes	No	N/A	7.  Is spill control and containment equipment (i.e. absorbents)

Env-Wq 401.04(g)		available in the outdoor storage area?

*	Yes	No	N/A	8.  Are regulated substances that are stored outside covered? (A cover must be permanent and large enough

to keep a container fully protected from rain and snow.)	Env-Wq 401.04(h)(2)

Describe: __________________________________________                                            ____________________________________________

*	Yes	No	N/A	9.  Are regulated substances which are stored outside > 50 feet from a surface water body or

Env-Wq 401.04(h)(4)	     > 75 feet from a private well?

*	Yes	No	N/A	10.  Are regulated substances that are stored outside > 50 feet from a storm drain?

Env-Wq 401.04(h)(4)	       If no, is secondary containment present? ______________________________

*	Yes	No	N/A	11.  Are regulated substances in outdoor storage areas stored outside the protective radius

Env-Wq 401.04(h)(4)	       of public water supply wells?  (radius is usually 400' - contact 271-0688 with questions)

*	Yes	No	N/A	12.  Do regulated containers in outside storage areas have secondary containment?

Env-Wq 401.04(h)(1)

| Transfer (Handling) of Regulated Substances in outdoor storage areas (refer to Env-Wq 401.05) | During an inspection, it is important to find out and understand where and how the PCS handles regulated substances. Observe all areas where fluids are used, or moved to and from. |
| --- | --- |

*	Yes	No	N/A	13.  Are regulated substances in outdoor storage areas transferred using funnels and drip pans or

Env-Wq 401.05(a)              other spill-safe devices?

*	Yes	No	N/A	14.  Are regulated substances in outdoor storage areas transferred over impervious surfaces?

Env-Wq 401.05(b)	       Describe: ____________________________________________________________________

_____________________________________________________________________

Section 5.

Regulated Substance Storage Areas (continued)

Release response information should be easy to find, clearly visible, and easy to read. If necessary, give a blank NHDES response form to the PCS contact. The form works best if copied onto brightly colored paper and placed in a clear plastic sleeve.

Release Response Information

(refer to Env-Wq 401.09)

*	Yes	No	N/A	15.  Is there adequate information posted at each outdoor storage area that indicates what should 		Env-Wq 401.09(b) 	       be done and who should be contacted in the event of a spill or other emergency?

Yes	No	N/A	16.  Did you recommend to the PCS that they post the NHDES release response form in outdoor 					                 storage areas?

Step C.  Questions to ask when observing indoor storage areas.

Storage of Regulated Substances in Indoor Storage Areas (refer to Env-Wq 401.04).

*	Yes	No	N/A	1.  Does the indoor storage area(s) have an impervious surface under the regulated substances?

Env-Wq 401.04(b)	     Describe: _____________________________________________________________________

*	Yes	No 	N/A	2.  Is the indoor storage area(s) secured against unauthorized entry (locked building, etc.)?

Env-Wq 401.04(c)	     Describe: _____________________________________________________________________

*	Yes	No 	N/A	3.  Is the indoor storage area(s) inspected weekly for signs of spills?

Env-Wq 401.04(d)

*	Yes	No 	N/A	4.  Is there sufficient space between large containers to allow for inspections?

Env-Wq 401.04(d)

*	Yes	No	N/A	5.  Is each regulated container clearly and visibly labeled with the name of material?

Env-Wq 401.04(e)

*	Yes	No	N/A	6.  Is each container closed and sealed or equipped with a drip pan beneath a spigot or pump?

Env-Wq 401.04(f)

*	Yes	No	N/A	7.  Is spill control and containment equipment (i.e. absorbents) available in the indoor storage area?

Env-Wq 401.04(g)

Transfer (Handling) of Regulated Substances in indoor storage areas (refer to Env-Wq 401.05)

*	Yes	No	N/A	8.  Are regulated substances in indoor storage areas transferred using funnels and drip pans or

Env-Wq 401.05(a)	     other spill-safe devices?

*	Yes	No	N/A	9.  Are regulated substances in indoor storage areas transferred over impervious surfaces?

Env-Wq 401.05(b)	     Describe: ___________________________________________________________________________

____________________________________________________________________________

Release Response Information in indoor storage areas (refer to Env-Wq 401.09)

*	Yes	No	N/A	10.  Is there adequate information posted at each storage area that indicates what should be done 		Env-Wq 401.09(b) 	       and who should be contacted in the event of a spill or other emergency?

Yes	No	N/A	11.  Did you recommend to the PCS that they post the NHDES release response form in indoor storage 					      		areas?

| Section 6. Floor Drains and Work Sinks | Floor drains can be small and easily hidden from view, so be sure to ask the PCS contact if any floor drains are present at the facility. Do not assume that you will observe all drains. |
| --- | --- |

Floor drains and work sinks are focuses of the BMP rules because they can be means by which hazardous substances are released to the environment. It is vital to know where floor drains and work sinks discharge. PCS background information is useful here because floor drains in an older building are more likely to discharge to a drywell or to an unknown point than those in a newer building. Env-Wq 402.07 prohibits discharges through floor drains to the environment. For this section, you need to know if the PCS is serviced by a sanitary sewer or by a septic system. Keep in mind that floor drains can range in size from circular drains a few inches in diameter to trench drains many feet in length.

Step A. Floor Drains (refer to Env-Wq 401.06)

Observe each floor drain for visible stains.  Note any stains in the chart below.

Answer questions 1 - 6 below

Yes	No	1.  Is the facility connected to a sanitary sewer?

Yes	No	2.  Are there any on-site septic systems?

Yes	No	3.  Are there any floor drains at the facility?

Concentrate on floor drains located near regulated substances. Drains in non-hazardous areas like bathrooms, kitchens or cafeterias are not covered by the Env-Wq 401 BMP rules.

If you answered “YES” to 3., above, list their locations and briefly describe, below:

List of Floor Drains at the PCS

| 1. | 4. |
| --- | --- |
| 2. | 5. |
| 3. | 6. |

Floor Drain Discharge Points (circle all that apply and describe in the box)

Unknown	   Holding Tank   	        Sanitary Sewer		 Septic System		     Drywell			Stream or Wetland

Yes	No	N/A	4.  If you circled unknown above, did you require that the PCS determine the discharge point of their floor 							drains?

*	Yes	No	N/A	5.  Are the floor drains authorized to discharge by any of the following (check all that apply)?

Env-Wq 401.06

| ____ Underground Injection Control (UIC) Registration | ___ National Pollution Discharge Elimination System Permit |
| --- | --- |
| ____ Holding Tank Registration | Other: |
| ____ Discharge Authorization from local treatment plant | Other: |

Yes 	No	N/A	6.  Did you ask to see the permits to verify their existence?

| Section 6. Floor Drains and Work Sinks (continued) | Floor drains and work sinks cannot discharge into or onto the ground or water without a permit. |
| --- | --- |

Env-Wq 401.03(k) defines work sink as a basin necessary to perform a task or process that requires a regulated substance, such as parts washing. Sinks used exclusively for hand washing are excluded from the inspection unless they are stained or located near where regulated substances are used. Observe sinks for visible staining. Many facilities have devices for parts cleaning that utilize a self-contained, recirculating system for degreasing solvent. Consider these devices a work sink, but note the self-containment feature in the chart below. Self-contained degreasing sinks comply with BMP rules.

Step B. Work Sinks (refer to Env-Wq 401.07)

Answer questions 1 - 4 below.

Yes	No		1.  Are there any work sinks used for non-hand washing purposes at the facility?

If you answered “YES” to question 1, list their locations and briefly describe, below:

List of Work Sinks at the PCS

| 1. | 4. |
| --- | --- |
| 2. | 5. |
| 3. | 6. |

Work Sink Discharge Points (circle all that apply and describe in the box)

Unknown	  Holding Tank	 Self-Contained	Sanitary Sewer	 Septic System	   Drywell		Stream or Wetland

Yes	No	N/A	2.  If you circled unknown, above, did you require that the PCS determine the discharge point of 					            their work sinks? Report all unknown discharge locations to the NHDES/UIC Program at (603) 271-2858.

*	Yes 	No	N/A	3.  Are all the work sinks authorized to discharge by any of the following (check all that apply)?

Env-Wq 401.07

| _____ Underground Injection Control (UIC) Registration | ____ National Pollution Discharge Elimination System Permit |
| --- | --- |
| _____ Holding Tank Registration | Other |
| _____ Discharge authorization from local treatment plant | Other |

Yes 	No	N/A	4.  Did you ask to see the permits to verify their existence?

| Section 7. Storage Tanks | Underground tanks cannot be directly observed, so simply list them and check their registration status. Observe all fueling areas. Keep in mind that the Env-Wq 401 BMP rules require that fueling be conducted on an impervious surface. |
| --- | --- |

Storage tanks are either underground or aboveground. A tank is considered underground if more than 10% of its capacity is below grade. The Env-Wq 401 BMP rules do not encompass all regulations pertaining to tanks; both underground and aboveground tanks are regulated apart from the BMP rules. However, because tanks have the potential to adversely impact the environment you must observe all PCS tanks and associated fueling and filling areas during an inspection. List all tanks at the PCS and find out if they are registered with the NHDES. BMP issues applicable to tanks may include impervious surfaces, secondary containment, covers, and setbacks from surface water and wells. Be sure to keep these issues in mind while observing tanks.

Step A. Underground Storage Tanks (USTs)

USTs are regulated by NH UST rules Env-Or 400.

##### Partial Summary of UST Regulations

- Non-residential USTs that contain other regulated materials (such as gasoline or chemicals) and are larger than 110 gallons must be registered with the NHDES.

- Non-residential heating oil USTs that are larger than 110 gallons must be registered with the NHDES if other USTs are on the site that must be registered.

Answer questions 1 - 6 below.

Yes	No	1.  Are any USTs located at the PCS?  If “YES,” list them below.

List of USTs at the PCS

| Contents | Capacity (gal.) | Age | Contents | Capacity (gal.) | Age |
| --- | --- | --- | --- | --- | --- |
| 1. |  |  | 5. |  |  |
| 2. |  |  | 6. |  |  |
| 3. |  |  | 7. |  |  |
| 4. |  |  | 8. |  |  |

*	Yes	No	N/A	Unknown  		2. Are the USTs at the PCS registered with NHDES?

Env-Wm 1401

Yes	No	N/A.			3. If you answered “unknown” or “no” to question 2, did you require the PCS to 								   		 determine or correct its UST registration status, if applicable?

*	Yes	No	N/A			4.  Does the PCS conduct fueling operations from its USTs over an impervious surface?		Env-Wq 401.04(b)

*	Yes	No	N/A			5.  Is spill control and containment equipment (i.e. absorbents) available near the USTs

Env-Wq 401.04(g)				    	 (especially where fueling takes place)?

*	Yes	No	N/A			6.  Is release response information posted near the USTs?

Env-Wq 401.09

| Section 7. Storage Tanks (continued) |  |
| --- | --- |

Step B. Aboveground Storage Tanks (ASTs)

ASTs are regulated by NH AST rules Env-Or 300.

Partial Summary of AST Regulations

•	A single AST with a capacity larger than 660 gallons must be registered with the NHDES.

•	Two or more ASTs with a total storage capacity larger than 1,320 gallons must be registered with NHDES.

•	ASTs with a capacity of 10,000 gallons or less storing fuel oil used only to heat an on-site structure do not have to be registered.

•	ASTs with a capacity less than 660 gallons are subject to BMP rules.

Answer questions 1 - 8 below.

Yes	No	1.  Are any ASTs at the PCS?  If “YES,” list below

List of ASTs at the PCS

| Contents | Capacity (gal.) | Age | Contents | Capacity (gal.) | Age |
| --- | --- | --- | --- | --- | --- |
| 1. |  |  | 5. |  |  |
| 2. |  |  | 6. |  |  |
| 3. |  |  | 7. |  |  |
| 4. |  |  | 8. |  |  |

*	Yes	No	N/A	Unknown		2.  Are the ASTs at the PCS registered with NHDES?

Env-Wm 1402

Yes	No	N/A.			3.  If you answered “unknown” or “no” above, did you require the PCS to determine 									or correct its AST registration status, if applicable?

*	Yes	No	N/A			4.  Does the PCS conduct fueling operations from its ASTs over an impervious surface?		Env-Wq 401.04(b)

*	Yes	No	N/A			5.  Is release response information posted near the ASTs?

Env-Wq 401.09

*	Yes	No	N/A			6.  Is spill control and containment equipment (i.e. absorbents) available near the ASTs?

Env-Wq 401.04(g)

*	Yes	No	N/A			7.  Do the ASTs at the PCS (including those that do not require registration) have a cover

Env-Wq 401.04(h)(1)			 		(i.e. roof) if outside, secondary containment and/or a spill prevention control and countermeasure plan (SPCC)?  Describe below.

___________________________________________________________________

___________________________________________________________________

*	Yes	No	N/A			8.  Do all portable, outdoor ASTs meet the BMP setbacks from surface water (>50 		Env-Wq 401.04(h)(4)				feet) and private wells (>75 feet)?  If no, describe below.

______________________________________________________________________

______________________________________________________________________

| Section 8. Final Questions | Fill out this section before you leave the site. Don’t rely on your memory to complete this form. Site specific information is easy to forget or to confuse with other facilities so fill out this form completely and have all your questions answered before leaving. |
| --- | --- |

Yes	No		1.  Do any on-site septic system(s) or drywell(s) accept any non-sanitary discharges not previously 			                  			 mentioned?  If yes, describe below.

_____________________________________________________________________________________________________

_____________________________________________________________________________________________________

Yes	No		2.  Are there any other non-sanitary discharges not previously mentioned?  If yes, describe below.

_____________________________________________________________________________________________________

_____________________________________________________________________________________________________

Yes	No		3.  Did the inspection indicate any other practices or findings that you want to discuss with NHDES? 		               		    		 If yes, describe below and call (603) 271-0688 for further assistance.

_____________________________________________________________________________________________________

_____________________________________________________________________________________________________

_____________________________________________________________________________________________________

| Section 9. Follow-up Procedures | Before you leave the site, inform the PCS representative that within 30 days you will get back to them in writing with the results of the inspection. |
| --- | --- |

- If you circled “No” to any question with an asterisk (*) beside it, or circled “Yes” to any question in Section 8, then the PCS is not in compliance with the referenced BMP or tank rule.

- If a BMP is not in compliance with a BMP or tank rule, you should notify them in writing within 30 days of the inspection. Written notification should include suggestions about how to correct non-compliance issues as well as reasonable deadlines. Refer to the booklet “Managing Groundwater Protection Areas - Guidance and Sample Letters” for assistance. Call NHDES at (603) 271-0688 for a copy.

- A PCS should be notified in writing within 30 days even if no BMP rule violations were observed.

- It is not necessary to submit copies of completed inspection forms to NHDES. However, be certain to keep them in your files for reference. A copy of a completed inspection form can be provided to a PCS if requested.

Please contact the NHDES Source Water Protection Program

by phone at (603) 271-0688 or by email at: chemwaivers@des.nh.gov

if you need training, assistance or have any questions.